## Slide 1
Project: First Monthly Progress Report (CA-2)
“EdgeGuard”
Guided By:
Dr. Deepak Dharrao
Guide, Dept. of Computer Engineering
Mourno Mahamat – PRN 23070122250
Lauriane – PRN 23070122260
Bokhit Mahamat – PRN 23070122249
Group Number: Group – 52
Department of Computer Engineering | Academic Year 2025–26
AI-Powered, Edge-Computing Safety Monitoring for Construction Sites — PPE, Worker-Fall & Object-Fall Detection

## Slide 2: Contents
Introduction
Motivation
Status of Current Work
Research Gaps
Problem-to-design mapping as per the GAP identified
System architecture diagram & Database Connectivity
Identified tools/technologies
Plan of Next Work
Conclusion
References

## Slide 3: Introduction
EdgeGuard (formerly SiteGuard) is a real-time, AI-powered safety-monitoring system for construction sites, built around an edge-computing-first design.
Watches a live webcam feed, an uploaded video, or a single image; detects every worker in frame and tracks them persistently.
Multi-item PPE compliance: helmet, vest, gloves, boots, and mask — checked per worker, per frame.
Worker-down detection: a dedicated fall classifier flags a fallen worker as a distinct, higher-severity event.
Falling-object detection: planned for the next phase, via tracked-object velocity analysis.
Full-stack web dashboard: live alerts, persistent worker log, session history, CSV/JSON export.

## Slide 4: Motivation
OSHA's “Fatal Four” — falls, struck-by, caught-in/between, and electrocution — remain the leading causes of construction-worker fatalities.
Manual monitoring doesn't scale: a site supervisor cannot watch every worker, on every task, at every hour — attention is finite; a camera feed is not.
PPE compliance is the most basic, most preventable safety control — and the easiest one to silently slip on.
Why edge computing: cloud-only inference adds latency, needs constant connectivity, and raises privacy concerns over on-site footage — motivating models light enough to eventually run on-site, not only in the cloud.

## Slide 5: Status of Current Work
ML pipeline complete end to end: YOLO26n person + PPE detection, ByteTrack tracking, two independent fine-tuned ViT classifiers (PPE items, fallen state).
YOLO26n trained on a merged 9,515-image detection set (7,611 train / 1,904 val): mean precision 0.79, recall 0.67, mAP@50 0.72.
ViT PPE classifier trained on 16,025 images (13,622 train / 2,403 val) with masked multi-label loss + per-label class weighting: macro-F1 0.866 (mask alone: 0.522 → 0.800).
ViT fall classifier trained on merged public fall datasets: 0.997 val macro-F1 — flagged as inflated by a training-domain gap and currently being corrected (see Research Gaps).
Full-stack app live: Node.js + Express + WebSocket dashboard, JWT auth + bcrypt + rate limiting, persistent SQLite logging with evidence snapshots.
Demo Mode fallback (colour + geometry heuristic) keeps the whole app runnable and demonstrable even without trained weights.
Local Intel Arc (XPU) GPU acceleration validated for training and inference, alongside Google Colab (T4) for full training runs.

## Slide 6: Research Gaps
No single public dataset labels all five PPE items jointly — available sources only overlap partially.
A single flattened accuracy/F1 score hides rare-label weaknesses (mask, at ~1% positive rate, looked fine until inspected per-label).
YOLO12n's attention-heavy architecture proved unstable on Intel XPU hardware (a reproducible device-lost crash) — a gap between published benchmarks and this project's actual target hardware.
No public “worker-fall” dataset exists for construction sites — the nearest available data is generic pedestrian/surveillance fall footage.
That domain mismatch causes real false positives: a model trained only on generic pedestrian imagery misclassifies real construction-worker photos (groups, PPE, tools) as “fallen.”
The UI compounded this: it hid the (correct) PPE reading whenever “fallen” fired — a good detection hidden behind a wrong one.

## Slide 7: Problem-to-Design Mapping as per the GAP Identified
Gap Identified | Design Response
Datasets don't jointly cover all 5 PPE labels | Masked multi-label BCE loss — blank cells excluded from loss/metrics via an explicit per-row label mask
Rare-label weakness invisible in one flattened score | Per-label F1 reported every epoch; “best” checkpoint now selected by macro-F1, not a flattened aggregate
Class imbalance hurt whichever label was rare | Automatic per-label pos_weight (neg/pos ratio, capped 10×) inside BCEWithLogitsLoss
YOLO12n unstable on target (XPU) hardware | Switched detector to YOLO26n, per Ultralytics' own attention/stability trade-off documentation
No construction-specific fall dataset | Merged two public Roboflow fall datasets; added the existing PPE dataset's images as free, domain-matched “not fallen” negatives
False “fallen” hid correct PPE detections | Worker-box label redesigned to show fallen status and PPE status together — never one overriding the other

## Slide 8: System Architecture Diagram & Database Connectivity
Webcam
Uploaded Video
Uploaded Image
Node.js + Express Server (pythonBridge.js spawns worker)
Python Inference Worker
YOLO26n Person Detect + ByteTrack Tracking
ViT PPE Classifier (5 labels)
ViT Fall Classifier (fallen)
Compliance + Alert Logic (per-worker history, debounce)
WebSocket (ws) Broadcast
Browser Dashboard (live feed, alerts, worker log, exports)
JWT + bcrypt Auth
SQLite (sql.js)
users · sessions · worker_history · violations + snapshots

## Slide 9: Identified Tools / Technologies
Tool / Technology | Role | Why Chosen
YOLO26n (Ultralytics) | Person + PPE-item box detection | Real-time at nano size; YOLO12n crashed reproducibly on our XPU hardware per Ultralytics' own attention/stability trade-off docs
PyTorch + Intel XPU backend | Training & inference runtime | Native Arc-GPU acceleration for local development, no cloud dependency required
HuggingFace Transformers (ViT) | Fine-tuned PPE & fall classifiers | Well-supported fine-tuning API over a pretrained ViT-base backbone; simple multi-label sigmoid head
ByteTrack (via Ultralytics) | Multi-object tracking | Associates low-confidence boxes; keeps worker IDs stable through brief occlusion
OpenCV | Frame decode, cropping, overlay drawing | De-facto standard, numpy-native, fast
Node.js + Express | Application server / REST API | Non-blocking I/O suited to concurrent streaming clients
ws (WebSocket) | Live dashboard push | Sub-100ms frame/alert delivery, far lower overhead than polling
SQLite (sql.js) | Persistent storage | Zero-ops embedded database; no separate DB server needed for a single-site deployment
JWT + bcrypt | Auth & session security | Stateless tokens + salted password hashing; standard practice for a multi-user dashboard
Google Colab (T4 GPU) | Training infrastructure | Free GPU access for full training runs beyond local hardware capacity

## Slide 10: Plan of Next Work
Finish the fall-model retrain with domain-matched negatives; re-validate directly against real construction photos, not just held-out splits from the same source datasets.
Complete the interrupted helmet-recovery ViT-PPE retrain (narrower augmentation) and reconcile it against the current checkpoint.
Object-fall detection: add a custom-labelled “object” class, retrain YOLO, and wire up the velocity-based fall trigger already scaffolded in config.
Move toward the “Edge” in EdgeGuard: profile and, where feasible, quantize the trained models for on-device inference.
Broader real-world validation: test across varied lighting/camera angles beyond the curated benchmark datasets.

## Slide 11: Conclusion
EdgeGuard now runs end to end — detection, tracking, PPE classification, and fall detection — with real trained weights live in the app for the first time this month, not just the Demo Mode heuristic.
Both successes and failures were measured honestly: the fall model's near-perfect validation score was investigated rather than accepted, and the domain gap it hid is already being corrected.
Working end-to-end pipeline
Trainable, not just pretrained
Honest, measured evaluation
Real-world gaps found and fixed, not just curated benchmarks

## Slide 12: References
Redmon, J., Divvala, S., Girshick, R., & Farhadi, A. “You Only Look Once: Unified, Real-Time Object Detection.” CVPR, 2016.
Dosovitskiy, A. et al. “An Image is Worth 16x16 Words: Transformers for Image Recognition at Scale.” ICLR, 2021.
Zhang, Y. et al. “ByteTrack: Multi-Object Tracking by Associating Every Detection Box.” ECCV, 2022.
Ultralytics. “Construction-PPE Dataset.” docs.ultralytics.com/datasets/detect/construction-ppe
Ahmad, M. et al. “SH17: A Dataset for Human Safety and PPE Detection in Manufacturing Industry.” (github.com/ahmadmughees/SH17dataset)
Roboflow public “fall-detection” and “person-fallen” datasets (used for ViT fall-classifier training data).
OSHA. Construction Industry “Fatal Four” hazard classification, U.S. Dept. of Labor.
Wolf, T. et al. “Transformers: State-of-the-Art Natural Language Processing.” Hugging Face, 2020.